RESPIRATORY EQUIPMENT CLEANING INSTRUCTIONS

CPAP/BIPAP MACHINE

MASKS

Daily Cleaning:  Wash the mask cushion with warm soapy water.  DO NOT use soaps with added scents.  Rinse well and allow to air dry out of direct sunlight

Weekly:  Separate and hand wash the mask components and headgear in warm, soapy water.

Biweekly:  Disinfect by soaking in one part household white vinegar and ten parts water.  Let it sit for 30 minutes and rinse thoroughly.

HEADGEAR

Weekly:  Hand wash in mild fabric detergent.  Allow to air dry.  Do not put in washing machine or dryer

Your headgear may be washed without being taken part

The dye used in the headgear my run during the first wash

TUBING

Weekly:  Wash in warm soapy water, rinse thoroughly, and then hang up and allow drying

Biweekly: Disinfect by soaking in one part household white vinegar and ten parts water.  Let it sit for 30 minutes and rinse thoroughly.

HUMIDIFIER CHAMBER

Two Times Weekly:  Wash with warm soapy water

Biweekly:  Disinfect by soaking in one part household white vinegar and ten parts water.  Let it sit for 30 minutes and rinse thoroughly.

FILTERS

Monthly:  Replace white filter.  Than cannot be cleaned.  DO NOT WASH THEM

Black foam filter:  If you have this, wash it with warm soapy water every week.  Rinse thoroughly and air dry before reusing	.

HUMIDIFIER SEAL

Monthly:  Disinfect by soaking in one part household white vinegar and ten parts water.  Let it sit for 30 minutes and rinse thoroughly.

CAUTION

Do not use solutions containing bleach, chlorine, alcohol, aromatics, moisturizers, antibacterial agents or scented oils to clean any part of the system or tubing.  These solutions may cause damage and reduce the life of the product.

Do not expose any part of the system or tubing to direct sunlight as it may deteriorate the product.

If any visible deterioration of the component is apparent (cracking, tears, etc.) the component should be discarded and replaced.